## Slide 1: Shale gas and fracking: fact and fiction
Mike Stephenson
British Geological Survey
Notes: Highlight science at the BSA festival

## Slide 2
Source: Nature Sept 2011
Fact
Fact
Notes: There are very few undisputed facts. Leave it at desciebing the ‘fact’

## Slide 3
Fact?
Methane in domestic water supplies from fracking?
…or natural methane?
Fact?
Notes: Shale gas as a subject is made up of contestable chunks of subject matter

## Slide 4
Cracks in a bridge from earthquakes caused by fracking
…or cracks that were already there
Fact?

## Slide 5
2006 to 2011, CO2 from fossil fuels declined by 7.7% due to substitution of shale gas for coal in power stations
Fact?
…but more greenhouse gas emissions due to ‘fugitive emissions’ of methane associated with fracking?

## Slide 6: Contestable areas in shale gas
Do shale gas wells contaminate groundwater?
Does fracking cause dangerous earthquakes?
Is shale gas lower carbon than coal?
Does fracking produce dangerous radioactivity?
Does shale gas use too much water?
Does shale gas cause subsidence?
Shale gas

## Slide 7
TRUE
FALSE
The science gauge
Peer reviewed scientific papers and projects can provide a ‘meter reading’
I’m going to show you how the ‘science gauge’ can be applied to some of these contestable issues.
Notes: The science meter can be applied to the contestable chunks of subject matter in shale gas

## Slide 8: Some shale and fracking basics

## Slide 9: Shale
1 mm
Grey or black, soft
Fine grained
70% of the world’s surface rocks are sedimentary; 50% of those are shale
Lots of organic matter (up to 10%)

## Slide 10
0.5 mm across

## Slide 11
Where the organic matter comes from

## Slide 12
Shale burial makes gas
Mud
Mud
Shale

## Slide 13
Gas in sandstone and shale
1 mm
sand grain
gas
gas
shale
sandstone
Shale grains

## Slide 14
Shale layer
Cracks the shale
High pressure water or nitrogen, 350-700 bar
Sand pumped in to hold cracks open
Fracking

## Slide 15
Credible regulation

## Slide 16
From Shale gas extraction in the UK: a review of hydraulic fracturing. The Royal Society and The Royal Academy of Engineering, Report DES2597.
Fracking site in Alberta

## Slide 17
Frack trucks

## Slide 18
Flowback tanks
Notes: Mnetion flow

## Slide 19
Truck carrying proppant

## Slide 20: Do shale gas wells contaminate groundwater? Some basics
TRUE
FALSE

## Slide 21
Water wells
Shale gas well
Water wells
Shale
biogenic methane released by bugs
Thermogenic methane released by fracking
Types of underground methane
Notes: Biogenic and thermogenic – d13C the way of telling them apart
Methane could be naturally occurring in the rock, before you test you have to know if there’s already methane there.
Methane moderately soluble, 0.054 µg/l,
increase at higher pressure
Natural methane in groundwater
  Chalk 0.05–42.9 µg/l,
  Triassic sandstone 0.05–465 µg/l
Different sources of thermogenic – stored gas, native gas

## Slide 22: Distinguishing biogenic and thermogenic
Notes: Biogenic/bacterial (e.g. wetland, landfill) – high C1/C2+ ratio, low δ13C values
Thermogenic (e.g. natural gas, coalbed methane) – low C1/C2+ ratio, higher (less negative) δ13C values

## Slide 23
Marcellus, Pennsylvania

## Slide 24: Contamination from fracking? Osborn et al. 2011, Duke University
Measured methane content and δ13C
Higher methane concentrations in water wells close to shale gas wells
δ13C suggests thermogenic
Authors then say ‘likely to be shale gas from the fracking’

## Slide 25: Water wells and shale wells
Water wells
Shale well
Shale well
Lots of criticism because the authors didn’t know how much natural methane there was in water wells before fracking…
and because the sample size was small
Notes: Gas wells are very deep 1500m
Water wells shallow 100m

## Slide 26
Dec 2011
Thermogenic methane unrelated to fracking?
Molofsky et al. 2013
Looked at some of the Osborn et al data
Also at baseline water data: historical records show flammable and effervescing natural springs and water wells back to the late 1700s.

## Slide 27
Molofsky et al. (2013).
Thermogenic methane related to topography?

## Slide 28
Molofsky et al. 2011
Methane signature indicates layers above Marcellus

## Slide 29
Duke University Group
Statistically significant evidence
141 water wells studied
methane concentrations six times higher for water wells within 1 km of shale gas wells
No correlation with topography (valleys)
Another look at the water wells Jackson et al. 2013

## Slide 30
Llewellyn et al. 2015
groundwater supply contamination incident
additives probably derived from drilling or hydraulic fracturing fluid were present in groundwater
Darrah et al. 2014
Noble gas and methane
Suggests leakage at intermediate depth due to casing and cement problems
Darrah et al. 2015
Noble gas, methane and other geochemistry
Outside shale gas areas
Diffusison of deep shale gas into shallow aquifers helped by neotectonic fracturing

## Slide 31
Shale gas well
Fault
Fault
Marcellus shale
Water well
Pennsylvania summary
Water well
Other shale layers
Natural
Leaking wells
Water well
Diffusion
Notes: Who’s right? Probably they’re both right…

## Slide 32
Shale gas wells do leak but only a small number…
And mostly in Pennsylvania….
Water contamination most likely from leaky wells - not fracking
Outside Pennsylvania
Duke University Group
127 drinking water wells
Fayetteville shale 4000 wells drilled since 2004
very low concentrations of methane
biogenic, not thermogenic
δ13C of the gas in the water wells was also distinct from the δ13C of the Fayetteville shale gas

## Slide 33: Is shale gas ‘lower carbon’ than coal? Some basics
TRUE
FALSE

## Slide 34
If 1400 natural gas power stations were substituted for an equal number of coal-fired power stations then this would save one wedge of CO2 emissions
Pacala and Socolow R 2004
Context

## Slide 35
Source US EIA

## Slide 36
But what about methane?
Open flowback tanks

## Slide 37
Shale gas well
Emissions from tank
‘Fugitive’ emissions
Shale layer
On the ground direct measurements
Notes: Biogenic and thermogenic
Methane could be naturally occurring in the rock
Methane moderately soluble, 0.054 µg/l,
increase at higher pressure
Natural methane in groundwater
  Chalk 0.05–42.9 µg/l,
  Triassic sandstone 0.05–465 µg/l
Different sources of thermogenic – stored gas, native gas

## Slide 38
Howarth et al. 2011 (Cornell Uni)
direct measurements
3 to 8% of the total methane production escapes to the atmosphere through the lifetime of every shale gas well
This is enough leaking gas to really make a difference
Is shale gas is worse than coal?

## Slide 39
Cathles et al. 2012 (Cornell Uni) rebuttal
High leakage rates of Howarth unrepresentative?
(ten tests of wells drilled into the Haynesville shale)
Source (mainly scientific papers and reports) | Shale layer | Volume of Gas released during flowback (thousands of cubic metres per well)
Jiang | Marcellus | 603
Howarth | Haynesville | 6800
Howarth | Barnett | 370
EPA | Various | 260
O’Sullivan and Paltsev | Haynesville | 1180
O’Sullivan and Paltsev | Barnett | 273
O’Sullivan and Paltsev | Fayetteville | 296
O’Sullivan and Paltsev | Marcellus | 405
O’Sullivan and Paltsev | Woodford | 487
from McKay and Stone (2013).

## Slide 40
Allen et al. 2014 (Uni Texas)
Direct measurement of 190 shale gas sites all over the US
leakage rate is about half of one percent of gas production,
much less than the 3 to 8% estimated by Howarth
Howarth et al
3 to 8%
Allen et al
<0.5%

## Slide 41
Howard (2015)
Allen et al. 2014 underestimated emissions
They used the Bacharach Hi- Flow® Sampler which in previous studies has been shown to exhibit sensor failures
The BHFS measurements at these sites were too low by factors of three to five

## Slide 42
Yes, in Pennsylvania, but in a small number of cases
Fracking doesn't seem to cause it directly
Other areas of the USA don’t seem to be affected
It might be to do with the cement completion of the well
Jury’s out

## Slide 43: Conclusions
The ‘science gauge’ can be applied to the contestable issues in shale gas
Science is important to society and not just big telescopes and synchrotrons!

## Slide 44
New book out now
TRUE
FALSE
Free summary paper